## Slide 1: Thermostat
Projects and laboratory on communication systems 2018/2019
Students:
Paolo Calao, Samuele Yves Cerini, Federico Pozzana
1

## Slide 2
Outline
Introduction
GUI and User Experience
  Welcome Window
  System Settings
  Room Functionalities
  Program timetable Definition
Backend SW and Web Interface
  Web interface
  RPi core logic
  RPi Database manager
  RPi Connection manager
Hardware
  Motivations
  Example of compliance
  Types of ESPs
  MQTT Topic
2

## Slide 3
Introduction – A Top-Down Approach
GUI and UX
3
Backend SW Logic
External Devices

## Slide 4
GUI and User Experience
4
Goal: provide a simple but functional interface for the end user
How: functionalities over fancyness, easy of use is a top priority
What we provide:
    An On-Board Graphical User Interface (PyQT5 Framework)
    A Web User Interface accessible from the home Local Network

## Slide 5
Welcome Window
5
Available Modes:
  Programmable
  Manual
  WeekEnd
  AntiFreeze
Seasons:
  Winter
  Summer
Room Slideshow
  The welcome window changes dinamically following the Actual Room displayed

## Slide 6
System Settings
6
Network:
  Connection to Home WiFi network
  SSID + Password
  Linux tools: wpa_supplicant, iw, ping
Room:
  Add/Delete Room
  Mnemonic (ex. "Kitchen")
  Deleting a room will logically delete all actuators and valves connected to it
Actuator:
  Unique ID
  An Actuator will be connected to valves that will handle the heating pipes

## Slide 7
Room Functionalities
7
Sensor:
  Collects temperature for the actual room
  Temperature is displayed in Welcome Window
Valves:
  An Actuator will drive a set of valves
  Valves will be turned on/off iff "Winter" mode is activated
AirConditioner:
  Module used to drive an AirConditioner, iff "Summer" mode is activated
  IR Blaster
Program
  Timetable definition

## Slide 8
Program Timetable Definition
8
Program:
  Working Days + Weekend
    Morning Temperature
    Evening Temperature
    Night Temperature
  Program is activated iff "Program" Mode is enabled

## Slide 9
Web interface reachable from devices in the same local network of the Raspberry.
It allows the customer to monitor temperatures and setup, and to change rooms settings. Also some graphs are shown.
Server-Side
M-DNS allow the access to the web Interface using the hostname ‘http://thermostat.local’
Apache2 + PHP
REST API to access thermostat status, configuration and temperatures.
Web Interface
Client-Side
Javascript framework called AngularJS
Single page application, only data structures are reloaded
9

## Slide 10
Raspberry
Central component of the system, gives life to devices interactions
Retrieve all temperature messages
Decides which actuator must be driven their working mode
RPi core logic
Needs a communication channel, in order to control the flow of messages
Needs a Storage to save and retrieve interesting informations
Storage
(DB manager)
Connection Manager
Core Logic
Actuator 1
Actuator 2
Sensor 1
10

## Slide 11
Database Manager
Common source of interesting informations for every component of the system
Informations always updated and shared, race conditions avoided
NoSQL DB stores informations in documents, format used to send messages. No data manipulation needed.
RPi Database Manager
Web Interface
GUI
Core Logic
DB
11

## Slide 12
Raspberry
Connection Manager
MQTT protocol adopted to allow devices communication
MDNS is exploited in order to make the raspberry reachable from its local net
The MQTT broker resides in the RPi, Mosquitto was used
RPi Connection Manager
Connection Manager component is used by the logic for subscribing/publishing
MQTT broker
Actuator 1
Actuator 2
Sensor 1
Local network
12

## Slide 13
Hardware used
ESP32 board
DHT22 temperature sensor
Relè module
IR transmitter and receiver
Li-Ion batteries and relative circuit
13

## Slide 14
Motivations
All the components used in this project respect this requirements
Availability among group members
Availability of libraries on the intenet (see DHT22)
In any case all the components had to be compliant with the project specifications
14

## Slide 15
Example of compliance
Project specification : Temperature must be controlled in the range from -10 °C up to +40 °C with an accuracy of 0,5 °C
DHT22 accuracy and range : 0.5 °C accuracy, range -40 °C up to 80 °C
DHT11 accuracy and range : 1 °C accuracy, range 0 °C up to 50 °C
Our choice was the DHT22 due to the previous reasons
15

## Slide 16
Types of ESPs
ESP used as sensor : this ESP uses the DHT22 to sense the current temperature, it publishes the result on the topic "temperatures"
ESP used as valve actuator : this ESP is connected to the relay module, it is firstly subscribed to the topic "actuator/configuration" where it is informed about the corrispondance between a valve and a room, and then it is dynamically subscribed to the topic "actuator/hot/roomID" where room ID is a number which describe the room/rooms currently configured
ESP used as IR actuator : this ESP is connected to both IR transmitter and IR receiver, it is dynamically subscribed to the topic "actuator/cold/roomID" where room ID is a number which describe the room in which the ESP is linked to
16

## Slide 17
MQTT topic used
Each ESP32 subscribe/publish to different topic depending on its function
ESP32 as sensor : publish on topic temperatures
ESP32 as IR actuator : subscribed to topic actuator/cold/roomID
ESP32 as valve actuator : subscribed to topic actuator/configuration and actuator/configuration/roomID
17

## Slide 18: Thanks for the attention