## Slide 1: Thermostat
Projects and laboratory on communication systems 2018/2019
Students:
1

## Slide 2
Outline
Introduction
Topic 1
Topic2
Topic 3
Topic 4
2

## Slide 3
Introduction – A Top-Down Approach
GUI and UX
3
Backend SW Logic
External Devices

## Slide 4
GUI and User Experience
4
Goal: provide a simple but functional interface for the end user
How: functionalities over fancyness easy of use is a top priority
What we provide:
    An On-Board Graphical User Interface (PyQT5 Framework)
    A Web User Interface accessible from the home Local Network

## Slide 5
Welcome Window
5
Available Modes:
  Programmable
  Manual
  WeekEnd
  AntiFreeze
Seasons:
  Winter
  Summer
Room Slideshow

## Slide 6
Room Functionalities
6
Network:
  Connection to Home WiFi network
  SSID + Password
  Linux tools: wpa_supplicant, iw, ping
Room:
  Add/Delete Room
  Mnemonic (ex. "Kitchen")
  Deleting a room will logically delete all actuators and valves connected to it
Actuator:
  Unique ID
  Shares the same connection method with a Sensor

## Slide 7
Room Functionalities
7
Sensor:
  Unique ID
  Collect temperature of actual room
  Bluetooth during the connection phase
  WiFi + MQTT once connected
Valves:
  Unique ID, from 1 to 8
  Linked to an Actuator, which must be already visible to the system
  Summer
AirConditioner:
  Shares similar properties with a Sensor
  IR Blaster
Program
  Timetable definition

## Slide 8
Room Functionalities
8
Program:
  Working Days + Weekend
  Morning Temperature
  Evening Temperature
  Night Temperature
  Program is activated iff Program Mode is enabled

## Slide 9
Hardware used
ESP32 board
DHT22 temperature sensor
Relè module
IR transmitter and receiver
Li-Ion batteries and relative circuit
3

## Slide 10
Motivations
All the components used in this project respect this requirements
Availability among group members
Availability of libraries on the intenet (see DHT22)
In any case all the components had to be compliant with the project specifications
3

## Slide 11
Example of compliance
Project specification : Temperature must be controlled in the range from -10 °C up to +40 °C with an accuracy of 0,5 °C
DHT22 accuracy and range : 0.5 °C accuracy, range -40 °C up to 80 °C
DHT11 accuracy and range : 1 °C accuracy, range 0 °C up to 50 °C
Our choice was the DHT22 due to the previous reasons
3

## Slide 12
MQTT topic used
Each ESP32 subscribe/publish to different topic depending on its function
ESP32 as sensor : publish on topic temperatures
ESP32 as IR actuator : subscribed to topic actuator/cold/roomID
ESP32 as valve actuator : subscribed to topic actuator/configuration and actuator/configuration/roomID
3

## Slide 13
Example
Example
Example
SE3
SE3
SE3
Central component of the system, gives life to devices interactions
Retrieve all Temperature messages
Decides which actuator must be driven and its working mode
RPi core logic
Needs an access point to the broker, in order to control the messages flow
Needs a Storage to save and retrieve interesting informations

## Slide 14
Example
Example
Example
SE3
SE3
SE3
MQTT protocol adopted to allow devices communication
MDNS is exploited in order to make the raspberry reachable from its local net
The MQTT broker resides in the RPi, Mosquitto was used
RPi Connection Manager
Connection Manager component is used by the logic to subscribe/publish

## Slide 15
Example
Example
Example
SE3
SE3
SE3
Common source of interesting informations for every component of the system
Informations always updated and shared, race condition avoided
NoSQL DB stores informations in documents, format used to send messages. No data manipulation needed.
Rpi Database Manager

## Slide 16
..
Web Application
..

## Slide 17: Thanks for the attention